## Slide 1: A Method for Reducing Active and Leakage Power in Kogge-Stone Adder
VLSI Design – ECE6332
Elaheh Sadredini
Luonan Wang
December 02, 2014

## Slide 2: Motivation
  Power dissipation is a critical constraint
    Portable SoCs
  Adders
    Digital Signal Processors
    Other operations like subtraction, multiplication, …
Notes: portable system-on-achip
(SoC) designs for communication computing equipment
has made power dissipation a critical constraint.
Full adders are important components in applications such as digital signal processors (DSP) architectures and microprocessors. Apart from the basic addition adders also used in performing useful operations such as subtraction, multiplication, division, address calculation, etc. In most of these systems the adder lies in the critical path that determines the overall performance of the system. Furthermore, energy reduction of functional units is a very important concern for high-end superscalar processors. There are always tradeoff between power and delay

## Slide 3: Carry Look-ahead Adder

## Slide 4: Power Reduction with Header or Footer in CLA
Using 8-bit CLA built with 2 4-bit CLA
Using Ocean script to sweep through different width
width(nm) = 50, 100, 150, 200, …, 450, 500

## Slide 5: Measurement results with only footer
Chart: propagation delay(ps)
| 9.14 | 17.649999999999999 | 26.16 | 34.67 | 43.18 | 51.69 | 60.2 | 68.709999999999994 | 77.22 | 85.73
Column C | 210 | 203 | 194 | 187.6 | 183 | 179 | 176 | 173.6 | 171.6 | 169.9
width(nm) | power(pw) | delay(ps)
50 | 9.14 | 210
100 | 17.65 | 203
150 | 26.16 | 194
200 | 34.67 | 188
250 | 43.18 | 183
300 | 51.69 | 179
350 | 60.20 | 176
400 | 68.71 | 174
450 | 77.22 | 172
500 | 85.73 | 170

## Slide 6: Measurement results with only header
Chart: propagation delay(ps)
| 9.81 | 19.079999999999998 | 28.34 | 37.6 | 46.85 | 56.11 | 65.36 | 74.63 | 83.89 | 93.14
header delay(ps) | 210 | 202.2 | 195.9 | 191.2 | 187.4 | 184.2 | 181.5 | 179.2 | 176.3 | 175.5
width(nm) | power(pw) | delay(ps)
50 | 9.81 | 210
100 | 19.08 | 202
150 | 28.34 | 196
200 | 37.60 | 191
250 | 46.85 | 187
300 | 56.11 | 184
350 | 65.36 | 181
400 | 74.63 | 179
450 | 83.89 | 176
500 | 93.14 | 175

## Slide 7: Kogge Stone Adder (KSA)
Fig 1 . 16 bit KSA [1]
PG Generator
Dot Blocks
Sum Generator
Notes: The Kogge–Stone adder is a parallel prefix form carry look-ahead adder
is widely considered the fastest adder design possible. It is the common design for high-performance adders in industry
Symmetric pattern
3 parts
Dominant block is Dot block
Where add sleep transistor? Where consume larger leakage and larger Active power
We have start with leakage power and calculate leakage for dot blocks for all possible inputs vectors  bar asase leakage power mirim jelo va badesh say mikonim active power ro kam konim

## Slide 8: Leakage Power in a Dot Block
P1 | P2 | G1 | G2 | Leakage Power (nw)
0 | 0 | 0 | 0 | 41.51
0 | 0 | 0 | 1.1 | 44.02
0 | 0 | 1.1 | 0 | 55.53
0 | 0 | 1.1 | 1.1 | 42.77
0 | 0 | 0 | 0 | 60.04
0 | 0 | 0 | 1.1 | 51.78
0 | 1.1 | 1.1 | 0 | 50.66
0 | 1.1 | 1.1 | 1.1 | 39.77
1.1 | 0 | 0 | 0 | 51.02
1.1 | 0 | 0 | 1.1 | 48.53
1.1 | 0 | 1.1 | 0 | 60.04
1.1 | 0 | 1.1 | 1.1 | 47.28
1.1 | 1.1 | 0 | 0 | 70.72
1.1 | 1.1 | 0 | 1.1 | 62.46
1.1 | 1.1 | 1.1 | 0 | 61.34
1.1 | 1.1 | 1.1 | 1.1 | 50.45
Table 1. Leakage power for all different input vector in a dot block
Notes: 0111 symmetric nist, pas 0000 ro entekhab mikonim

## Slide 9: Leakage power in KSA
Input vectors | Leakage Power (uw) | 
 | 8 bit KSA | 16 bit KSA
All ‘0’ | 1.89 | 4.48
All ‘1’ | 1.96 | 4.61
101010…1010 | 1.96 | 5.97
Table 1. Leakage power for KSA

## Slide 10: Worst leakage power consumption?
Fig 2. Number of having P1P2G1G2=1100 for each dot block input in 8 bit KSA
Count
Bit index
Dot block level
P2=P1=1, G1=G2=0
Notes: SystemC

## Slide 11: Best Place for Adding Sleep Transistor
First level Dot block
  Simulation results
  Number of Dot block
    It is more possible to save both leakage and active power
  Near to PG generators
Notes: First, the simulation result shows that that first level KSA adder have more potential for consuming leakage power.
Second, the number of dot blocks is larger in the first level and if we use our low power technique, it is more possible to save both dynamic and static power.
Tozihe raveshe pishnahadi: using sleep transistors for two purpose
Clk
Sleep Transistor  State retention

## Slide 12: Multi-mode Power Gating
Fig 3. Multi-mode sleep transistors: a. Normal mode, b. Cold mode, c. Park mode (intermediate power saving mode) [2]
Notes: Yeki az ravesh haye state retention ine
Killing two birds with one stone  dynamic and static
Fig. 1(a) shows our new power gating structure in RUN/IDLE
mode. In this mode, PG is asserted high to force the nMOS transistor
in the power gating structure into a low-resistance state,
while HLD is set high. The nMOS is used to short the virtual
ground VGND of the logic circuit to the real ground potential
GND, allowing the full supply voltageVDDto be applied across
the circuit, and thus permitting high-speed operation.
Fig. 1(b) shows the circuit in COLD mode, which does not
retain state. PG is held low while HDL is high, the current path
to GND is cut, and the voltage across the logic circuit collapses,
suppressing both gate and subthreshold leakage currents. As
the VGND node is close to VDD, the sources of the pulldown
network transistors are reverse-biased with respect to their body
connections which are held at GND. Drain-induced barrier
lowering (DIBL) causes an increase in the threshold voltage and
reduces the subthreshold leakage currents in the transistors of
the pulldown network [13], [14]. In the state-retention or PARK
mode, shown in Fig. 1(c), both PG and HLD are asserted low.
Consequently, the nMOS device is turned off and the pMOS
operates as a source-follower. In PARKmode, the virtual ground
railVGNDis held at a voltage above that of the ground rail,
where is the threshold voltage of the PMOS. The voltage
across the logic circuit becomes VDD- causing a reduction
in gate leakage and subthreshold leakage, since these leakages
are dependent on the voltage applied to the devices. In this mode,
the VGND voltage level is limited by . As a result, state
is retained, and the ground bounce induced by power mode
transitions is smaller than it is in COLD mode. PARK mode
can also be used as an intermediate step to reduce the ground
bounce induced by the transition from COLD to RUN/IDLE.

## Slide 13: Negative Clock Skew
∆
∆ =
Block | Delay (ps)
PG generator | 20
Dot block | 15
Sum generator | 20
Table 2. Delay calculation for different blocks in a 8-bit KSA
∆
Notes: How to generate clock for PG and HLD
Mazaya: Critical path ro ziad nemikone
Zamane Lazem Baraye dar oomadan az sleep ro dare
Hame Dot block va ham PG generator

## Slide 14: Leakage Power
Chart: Delay (ps)
| 165.23 | 164.76 | 163.25 | 162.34 | 161.56
 | 2.3753 | 2.5154 | 2.6734 | 2.8802 | 3.0134
Fig 4. Leakage Power for 8-bit KSA with different width in sleep transistor
 | Leakage P (uw) | Delay (ps)
Without Power Gating | 2.466 | 158
With Power Gating | 2.375 | 165.23

## Slide 15: Active Power
Chart: 
| 165.23 | 164.76 | 163.25 | 162.34 | 161.56
 | 263 | 263.2 | 263.6 | 263.8 | 264
 | Active P (uw) | Delay (ps)
Without Power Gating | 405 | 158
With Power Gating | 263 | 165.23
Fig 4. Active Power for 8-bit KSA with different width in sleep transistor

## Slide 16: Pros and Cons
Pros
  Reducing leakage power
  Reducing active power
Cons
  Delay into the critical path, but not that much
  Area

## Slide 17: Future Works
Having more than one clock skew and put more than one level into a PARK mode efficiently
Power-delay calculation for 16 bit, 32 bit KSA
Comparison with different parallel prefix adders

## Slide 18: Reference
[1] http://en.wikipedia.org/wiki/Kogge%E2%80%93Stone_adder
[2] Suhwan Kim ; Seoul Nat. Univ., Seoul ; Kosonocky, S.V. ; Knebel, D.R. ; Stawiasz, K., “A Multi-Mode Power Gating Structure for Low-Voltage Deep-Submicron CMOS ICs”, IEEE Transactions, IEEE Circuits and Systems Society, Volume:54 , Issue: 7, July 2007.
[3] Jan M. Rabaey, Anantha Chandrakasan, Borivoje Nikolic, “Digital Integrated Circuits: A Design Perspective”, Second Editon, 2003.

## Slide 19
Question?

## Slide 20
PG
PG
PG
PG
PG
PG
PG
PG
DOT
DOT
DOT
DOT
DOT
DOT
DOT
DOT
DOT
DOT
DOT
DOT
DOT
DOT
DOT
DOT
DOT
SUM
SUM
SUM
SUM
SUM
SUM
SUM
SUM